# Cost Effective Forth Systems in FPGAs
Sub-$10 FPGAs are considered:
## Gowin
Gowin Semiconductor is a China-based FPGA company started in 2014. Their GW1N series was introduced in 2017. They are available now, even for little guys, at a decent price. These FPGAs have some nice features for Forth-based systems:
- They're inexpensive.
- They're secure.
- Built-in flash is big enough for Forth apps in addition to the bitstream.
- You can get by with 1 or 2 LDOs depending on the part.
- There is an on-chip oscillator with 5% tolerance.

The GW1N-UV4 has about 5mA static power consumption with a single power supply. The GW1N-LV4 draws less power but needs an extra LDO for the core voltage. It fits the Forth CPU, some user logic, and 32KB of code in on-chip flash at a $3 to $4 price point. QFN and LQFP packages are available with 32 to 144 pins or more.
So, it's competitive with MCUs. Forth's instant bootup means you can cold-boot at wakeup. A pushbutton (or buttons) can trigger a simple power control circuit in battery-operated systems. Embedded Linux boots on one second if highly optimized, on the order of 10 if not. That's very slow for devices that should respond instantly.
FPGAs don't suffer from vendor lock-in. Granted, the internal flash interface requires some custom HDL code, but the opportunity for lock-in is much greater for today's MCUs. The vendors can raise their prices after enough design wins, knowing that the incredible complexity of their parts guarantees that customers can't just switch to another vendor.
The learning curve for MCUs with their vast array of peripherals and their options keeps rising to the point that it's faster to just roll your own peripheral.
The Gowin parts support LUT5 and LUT6 structures, leading me to think performance will be decent.
### Flash
Flash seems to be the main consideration. You want your code secure but upgradeable. This is where the flash memory comes in. The low end of code space sits in internal flash in the GW1N-LV4. What if your app is really big? Let it overflow to SPI flash. Of course, the interpreter will be able to dump out all of that internal flash, so the app can be read out and analyzed. That would leave cloners the job of reverse engineering all of the logic (undocumented peripherals). If you still don’t like those odds, the interpreter can be disabled by erasing the header space.
The GW1N internal flash is 32-bit with an access time of 25 to 50 ns. With a CPU clock of 10 ns, that’s 3 to 5 clock delays. This is good enough for simplified access with no prefetch.
According to the pinouts, SPI flash pins should be user I/O after configuration.
### DK-START-GW1N4 Development Board
I got V1.1 of the PCB. The IDE installed easily and I received the license files. The instructions weren’t very clear, but you need to edit environmental variable LM_LICENSE_FILE to point to the Symplicity license. Gowin gives you licenses that are good for one year. As of 6/2019, the tools are still in Beta.
I could download a sample file for this board. On my first try, the programmer didn’t like the device ID. I hit “scan” to read out the part type, selected that part, and re-synthesized. It downloaded into SRAM – yay! Cycling power made it go away, as expected. Putting the bitstream in flash also worked, so then the board booted up with the demo. Cool. The board also has a “reset” pushbutton input.
The tools are bare bones, which helps with the learning curve. The constraint file is very simple. Each line is pin and location. There’s no I/O standard or slew rate to select.
The board oscillator is 50 MHz, so to keep things simple I set up the Forth MCU to run at 50 MHz. For the P&R bitstream configuration, I set the SPI flash address to 0. The board flash is a W25Q64, so 64M bit (8M bytes). The FPGA needs at most 216K bytes, so the base address for Forth flash is set to 4 (starts at address 0x40000). The design synthesized to about 3K (out of 4K) LUTs and about 60 MHz. Unfortunately, the P&R tool hung on the synthesized netlist. Tool problem. I reported the bug.
## Efinix
Efinix Semiconductor is another Chinese FPGA company targeting the low-end space. Their parts are starting to enter the supply chain, so a little hard to get. This should change in the next year or two due to investment by Xilinx and Samsung. They have a novel FPGA architecture that costs less to make and has power and speed advantages over other FPGAs. Their roadmap to 10nm (backed by Samsung) is an eye opener. But let’s look at their current 40nm FPGAs, the Trion series.
If you build something with one of these, it will most likely boot from SPI flash. Security will have to be achieved by board level anti-cloning features such as a hardware security chip.
In this case, the Forth system will share SPI flash with the bitstream. These parts aren’t ready for prime time, so pinouts etc are hard to come by. Are the config pins GPIO after boot? Maybe revisit in 2020. There is a user JTAG TAP, so JTAG could be used to talk to the Forth core.
I would have to buy a dev board to get access to tools to synthesize with, so there’s no telling how results will pan out.
## Lattice
The ice40 series can boot from SPI flash or use internal OTP. So, production parts can be secure. I tried synthesizing the MCU and ended up with a clock speed of 40 MHz or so.
## Xilinx
The smallest Spartan 3 parts are under $10. You could boot those from SPI flash.
## Intel
Altera/Intel MAX10 is cheap, and offers internal flash. It doesn’t boot directly from SPI flash and the synthesis results weren’t the greatest. Package options are also a bit limited.