# SFIF: Serial NOR Flash Interface

sfif
26
caddr

32
cdata	NCS

cready	SCLK

8
4
config	data_o

4
drive_o
8

4
xdata_o	data_i

10

xdata_i

xtrig

xbusy

clk, reset

Generics:
RAMsize:	log2 of the number of 32-bit RAM words in "Internal ROM".
CacheSize: log2 of the number of 32-bit RAM words in the flash cache.
BaseAddr: The physical address of the first 64KB sector.

RAM resides at the bottom of the address range to provide faster access. It uses synchronous-read RAM. It gets loaded from flash after reset. It's assumed that the hardware reset was long enough to let the flash chip settle.

Cache is a small RAM that gets filled from the SPI bus starting at the first "hit" in the cache page and ending when the last word in cache is written. Code may loop backward while in the cache region to execute in this cache as long as it stays within the page. The cache should be kept somewhat small since it will fill whether or not you use all of it. 16 words is probably a good number.

BaseAddr is the number of the first 64K block. If non-zero, it allows the bottom of flash to contain the FPGA bitstream. For example, Xilinx 7A35T and 7A100T need 34 and 59 blocks (of 64KB) respectively for their bitstreams. BaseAddr could be 34 or 59. In practice, BaseAddress would be a power of two for compatibility with flash memory protection capabilities. So, in either case it would be 64. On an Arty A7, that leaves 192 for the app(s).
Data Rates
Single and Dual rates use two data lines. Quad rate uses four. A PCB that's set up for plain SPI can support dual-rate transfers. Connecting two more wires allows quad rate. Upon startup, an internal shadow RAM is loaded from flash using single-rate due to universal support for the "Fast Read" command format. Code for selecting higher rates will run in that to determine which dual or quad rate format the flash wants and to enable those modes.

Quad data rate needs to be enabled before the command will be accepted. The ability to override hardware write protect is off by default. It's a non-volatile configuration setting, like lots of other things. There's a lot to a newer flash chip and they all have their little quirks.

Modern flash lets you choose between legacy and QPI modes. The controller uses legacy modes for the sake of wider compatibility. Fetching from a new address uses 1-1-1, 1-2-2, or 1-4-4 encoding. The xdata port always uses 1-bit transfers so that a direction bit isn't needed. The cdata port has a programmable rate.

The number of system clock cycles per word read when SCLK = clk/2 as measured in simulation depends on whether the accesses are sequential and in-page or if a new page is accessed. With a 100 MHz clock, SCLK is 50 MHz. Cycles (throughput in MB/s):

Rate	In page	Out of page
Single	67 (12)	228 (3.5)
Dual	35 (23)	151 (5.3)
Quad	19 (42)	103 (7.7)

This was with the FMF model of the Spansion S25FL064L. The model's default CR1V was changed to QUAD=1 to enable quad rate.

The burst wraparound mode could be exploited to fill the cache, which would make sense for code that tends to jump backward before sequencing. Bit 0 of the configuration is reserved for this. A 64-byte wrap, when enabled, would fit a 16-word cache. This is one of those special features I didn't bother with. Jumping backward within the page will re-start filling. It's probably a good idea to keep the words that are already in the flash in such a case.

Most SPI flash parts support dual and quad read commands. The most straightforward strategy for a controller seems to be to rule out parts over 128M not supporting the EC command and use EB/EC for quad read. Use a programmable dummy cycle setting. Software can "feel out" the correct setting and/or change the flash's timing defaults. The controller boots up in single-bit mode. It's up to software to switch modes to something that suits the flash.

## A Protocol for Flash Programming
Most FPGA tools have a way to program user data into the SPI boot flash through the FPGA's JTAG. An ASIC will usually have JTAG too. But, since there is already a debug UART, that can be shared with programming hardware to enable field upgrades.

A stream-based system should reserve XON (11h) and XOFF (13h) for flow control. DLE (10h) is used for an escape sequence. DC2 (12h) is reserved for a sync character. The missing range of 10h to 13h is replaced by {10h 00h} through {10h 03h} to pass all 256 8-bit symbols.

{10h 0Fh 12h} starts an escape sequence that puts the MCU in reset and allows the UART to directly control the SPI port of the flash. ESC (1Bh) releases the reset. The trailing 12h is for detection of dropped characters.

"Ping" is 2Fh, which returns 3Dh if the flash is busy, 3Ch if not.

3Fh requests a 4-byte product ID that the host can use to verify that the flash image is made for that device.

The SPI transfer is controlled by a 10-bit symbol. The character range for the first symbol are {@ABCDEFGHIJKLMNOPQRSTUVWXYZ[\]^_} and {`abcdefghijklmnopqrstuvwxyz{|}~} for the second symbol. Each character pair triggers a SPI transfer and returns a 2-digit hex byte. The input symbol's bit 5 = '0' for the first byte(s), '1' for the second byte. Bit 6 = '1' for both bytes. Output symbols are 5xh, or {PQRSTUVWXYZ[\]^_}.

Programming software knows when to wait for a transfer or not, but the transfer occurs much faster than the baud rate so it won't get stepped on even without flow control. A slow bit rate like 115.2K will transfer 337 KB/min to/from the flash, excluding erase and programming times. Some parts have built-in CRC checking. The programming utility should exploit specific flash hardware features. It may also protect against OTP abuse and implement other security measures.

Since the UART is in the MCU module, integration with the flash programming protocol should be handled there too.
## SPI transfers
Serial Flash uses a “mode 0” SPI interface. The fastest SCLK is half the system clock frequency. The flash device clocks in data at the rising SCLK edge and outputs data at the falling edge.

Bits 8 and 9 of xdata_i control NCS before and after the SPI transfer. Bit 9 (first) deasserts CS for eight SCLK periods before starting the transfer. Bit 8 (last) deasserts CS after the transfer.

When a transfer is started, CS is automatically asserted. If last=1, CS is deasserted after the transfer completes. If first=1, CS is deasserted for eight SCLK cycles before the transfer. For most parts, this time tSHSL must be at least 100ns although some parts specify 50ns.

For double and quad rates, the data lines are bidirectional. Rather than using bidirectional I/O ports, each I/O line has separate input, output, and drive-enable lines.

## Simulation

The tb_sfif testbench connects the sfif module to a VHDL model of a Serial Flash. This model uses some tools from the Free Model Foundry that must be compiled first into a new library called FMF. The first thing to do in setting up a simulation is to create a new FMF library if it doesn't exist.

In ModelSim:
File > New > Library FMF
Change Properties of conversions.vhd: General Settings: Compile to library FMF
Change Properties of gen_utils.vhd: General Settings: Compile to library FMF
Change Properties of s25fl064l.vhd: Use 1993 syntax

The testbench model uses the following files:

Filename	Folder	Library	Contents
conversions.vhd	./testbenches	FMF	FMF stuff
gen_utils.vhd	./testbenches	FMF	FMF stuff
s25fl064l.vhd	./testbenches	work	Serial Flash (Cypress introduced in 2017)
spramEZ.vhd	.	work	Generic synthesizable RAM
sfif.vhd	.	work	Flash interface for Tiff MCU
tb_sfif.vhd	./testbenches	work	Testbench for sfif.vhd

The testbench expects the lower 1024 words (4KB) of flash to contain the data generated by spif.f, helf in testrom.txt. It requests runs of random-length data from random addresses and compares the returned data against its expected value.