# SFIF: Serial NOR Flash Interface

sfif
26
caddr

32
cdata	NCS

cready	SCLK

8
4
config	data_o

4
drive_o
8

4
xdata_o	data_i

10

xdata_i

xtrig

xbusy

clk, reset

config: 8-bit SPI configuration: set when b15='1'. The fields are:
{speed, rate, dummy, hasmode} in [7:6], [5:4], [3:2], and [1] respectively.

speed:	SPI interface speed: 0=--, 1=clk/2, 2=clk/4, 3=clk/8; Default = 3.
rate:	Select rate for all ROM reads: 0=single, 1=double, 2=quad; Default = 0.
dummy:	Number of dummy cycles to wait for read data: {4, 6, 8, 10}; Default = 2 (8).
hasmode:	Include a mode byte after the address: Default = 0.

The xdata port is used by the MCU to access the flash under software control. Hardware should use it to program the flash to make it unbrickable.

Generics:
RAMsize:	log2 of the number of 32-bit RAM words.
BaseAddr: The physical address of the first 64KB sector.

RAM resides at the bottom of the address range to provide faster access. It uses synchronous-read RAM. It gets loaded from flash after reset. It's assumed that the hardware reset was long enough to let the flash chip settle.

BaseAddr is the number of the first 64K block. If non-zero, it allows the bottom of flash to contain the FPGA bitstream. For example, Xilinx 7A35T and 7A100T need 34 and 59 blocks (of 64KB) respectively for their bitstreams. BaseAddr could be 34 or 59. In practice, BaseAddress would be a power of two for compatibility with flash memory protection capabilities. So, in either case it would be 64. On an Arty A7, that leaves 192 for the app(s).
## A Protocol for Flash Programming
Most FPGA tools have a way to program user data into the SPI boot flash through the FPGA's JTAG. An ASIC will usually have JTAG too. But, since there is already a debug UART, that can be shared with programming hardware to enable field upgrades.

A stream-based system should reserve XON (0x11) and XOFF (0x13) for flow control. DLE (0x10) is used for an escape sequence. DC2 (0x12) is reserved for a sync character. The missing range of 0x10 to 0x13 is replaced by {0x10 0x00} through {0x10 0x03} to pass all 256 8-bit symbols.

{0x10 0x0E 0x12} starts an escape sequence that puts the MCU in reset and allows the UART to directly control the SPI port of the flash. {0x10 0x0F 0x12} releases the reset. The trailing 0x12 is for detection of dropped characters.

The SPI transfer is controlled by a 10-bit symbol in base 32 format. The characters for each digit are {@ABCDEFGHIJKLMNOPQRSTUVWXYZ[\]^_} so each character pair triggers a SPI transfer and returns a 2-digit hex byte. Programming software knows when to wait for a transfer or not, but the transfer occurs much faster than the baud rate so it won't get stepped on even without flow control. A slow bit rate like 115.2K will transfer 337 KB/min to/from the flash, excluding erase and programming times. Some parts have built-in CRC checking. The programming utility should exploit specific flash hardware features.

Since the UART is in the MCU module, integration with the flash programming protocol should be handled there too.
## SPI transfers
Serial Flash uses a “mode 0” SPI interface. The fastest SCLK is half the system clock frequency. The flash device clocks in data at the rising SCLK edge and outputs data at the falling edge.

Bits 8 and 9 of xdata_i control NCS before and after the SPI transfer. Bit 9 (first) deasserts CS for eight SCLK periods before starting the transfer. Bit 8 (last) deasserts CS after the transfer.

When a transfer is started, CS is automatically asserted. If last=1, CS is deasserted after the transfer completes. If first=1, CS is deasserted for eight SCLK cycles before the transfer. For most parts, this time tSHSL must be at least 100ns although some parts specify 50ns.

For double and quad rates, the data lines are bidirectional. Rather than using bidirectional I/O ports, each I/O line has separate input, output, and drive-enable lines.
## Read Modes
There are many standard read modes. Some are supported by all flash parts, some aren't. The rate setting chooses which READ command will be used. "Extended SPI" is assumed. When reading in dual or quad rate mode, different parts use different numbers of dummy cycles between the address and data. It's a tradeoff between maximum operating frequency and number of dummy cycles.

All parts support Fast Read (0B). Most support 32-bit-address Fast Read (0Ch). The default is 8 dummy cycles.

Micron:
MT25QL512ABB:
EB/EC = quad fast read, 1-4-4, 10 dummy cycles after 24/32-bit address.
One could output a dummy Mode byte and 8 dummy cycles.

Winbond and Cypress:
BB/BC = dual fast read, 1-2-2, Mode4 and 2 (default) dummy cycles after 24/32-bit address.
EB/EC = quad fast read, 1-4-4, Mode8 and 4 dummy cycles after 24/32-bit address.
Mode should be Fxh, dummy is floating. Mode may be used to keep the command in 4-wire mode for future reads.

Macronix:
MX25L25735F:
BB = dual fast read, 1-2-2, 4 (default) dummy cycles after 24/32-bit address.
EC read not supported. Use EB with 32-bit address. Also uses the Mode byte. Bits DC0 and DC1 in the configuration register set the number of dummy cycles.
For EB read, the default is 6.

ISSI:
IS25LP256D:
0B/0C = single fast read, 1-1-1, 8 (default) dummy cycles after 24/32-bit address.
BB/BC = dual fast read, 1-2-2, Mode4 and 2 (default) dummy cycles after 24/32-bit address.
EB/EC = quad fast read, 1-4-4, Mode8 and 6 (default) dummy cycles after 24/32-bit address.

The most straightforward option seems to be to rule out parts over 128M not supporting the EC command and use EB/EC for quad read. Use a programmable dummy cycle setting. Software can "feel out" the correct setting and/or change the flash's timing defaults. The controller boots up in 1-wire mode at a slow speed. It's up to software to switch modes to something that suits the flash.
## Simulation

The tb_sfcon testbench connects the sfcon module to a VHDL model of a Serial Flash. This model uses some tools from the Free Model Foundation that must be compiled first into a new library called FMF. The first thing to do in setting up a simulation is to create a new FMF library if it doesn't exist.

In ModelSIM, you can add all of the files to the project and edit each file's properties to point them to the right libraries. Note that most files also need the "Use 1993 Language Syntax" box checked.

In Sonata, you can add the FMF files to the FMF (library) part of the workspace and the others to the main workspace. Drag the FMF library to the top so it compiles first.

The testbench model uses the following files in order:

Filename	Folder	Library	Contents
conversions.vhd	./bench	FMF	FMF stuff
gen_utils.vhd	./bench	FMF	FMF stuff
s25fl008a.vhd	./bench	work	Serial Flash model
sfcon.vhd	.	work	Wishbone interface to Serial Flash
tb_sfcon.vhd	./bench	work	Testbench for sfcon.vhd

The double and quad speed options have not been tested.